## Slide 1: MODULE 3 - Fundamentals of Computer Architecture Instruction Sets: Characteristics and Functions
Dr. A. Bhuvaneswari
Assistant Professor Sr.
VIT Chennai

## Slide 2: Instruction Set Architecture
Instruction Set
Software
Hardware

## Slide 3: ISA…

## Slide 4: Elements of an ISA…
Instructions
  Instruction Formats
  Addressing Modes
  Condition Codes
  Instruction sets

## Slide 5: What is an Instruction Set?
The complete collection of instructions that are understood by a CPU
Machine Code
Binary
Usually represented by assembly codes
Notes: 2

## Slide 6: Elements of an Instruction
Operation code (Op code)
  Do this
Source Operand reference
  To this
Result Operand reference
  Put the answer here
Next Instruction Reference
  When you have done that, do this...
Notes: 3

## Slide 7: Instruction Representation
In machine code each instruction has a unique bit pattern
For human consumption (well, programmers anyway) a symbolic representation is used
  e.g. ADD, SUB, LOAD
Operands can also be represented in this way
  ADD A,B
Notes: 5

## Slide 8: Instruction Cycle State Diagram
Instruction Fetch – Decode-Execute

## Slide 9: Simple Instruction Format

## Slide 12: Instruction Types
Data processing
Data storage (main memory)
Data movement (I/O)
Program flow control
Notes: 6

## Slide 13: INSTRUCTION FORMATS

## Slide 14: Number of Addresses (a)
3 addresses
  Operand 1, Operand 2, Result
  a = b + c;
  May be a forth - next instruction (usually implicit)
  Not common
  Needs very long words to hold everything
Notes: 7

## Slide 16: Number of Addresses (b)
2 addresses
  One address doubles as operand and result
  a = a + b
  Reduces length of instruction
  Requires some extra work
    Temporary storage to hold some results
Notes: 8

## Slide 18: Number of Addresses (c)
1 address
  Implicit second address
  Usually a register (accumulator)
  Common on early machines
Notes: 9

## Slide 20: Number of Addresses (d)
0 (zero) addresses
  All addresses implicit
  Uses a stack
  e.g. push a
  push b
  add
  pop c
  c = a + b
Notes: 10

## Slide 22: Characteristics of good ISA
Must be Clear
Less usage of complex instructions
Ease of compilation
Ease of implementation

## Slide 23: Instruction Formats…
A machine has 24 bits instruction format. It has 32 registers and each of which is 32 bit long. It needs to support 49 instructions. Each instruction has two register operands and one immediate operand. If the immediate operand is signed integer, then the minimum value of it can be ________?

## Slide 24: Instruction Formats…
A machine has 24 bits instruction format. It has 32 registers and each of which is 32 bit long. It needs to support 49 instructions. Each instruction has two register operands and one immediate operand. If the immediate operand is signed integer, then the minimum value of it can be ________?
Instruction = 24bits (opcode,reg1,reg2,immediate_operand)
Opcode implies the instruction number => 49 instructions can be represented using 6bits (26=64 instructions and 25=32 instructions )
32 Registers can be represented using 5bits (25=32)
2 registers in instruction = 10 bits
Immediate operand = 8 bits (24-6-5-5)
Signed integer for immediate operand hence range = -128 to 127
Hence, minimum value = -128

## Slide 25: Addressing Modes

## Slide 26: Prerequisite - Introduction to parts of CPU
Arithmetic and Logic Unit (ALU)
It performs all the arithmetic and logical micro operations.
Floating Point Unit (FPU)
It performs operations on floating point numbers.
Memory Unit (MU)
It stores the set of instructions.
Control Unit (CU)
It supervises the sequence of micro operations.
Registers
Temporary storage area, which holds the data during the execution of an instruction.
CU
FPU
MU
REGISTERS
ALU

## Slide 27: Prerequisite - Registers inside CPU
A (8-bit)
B (8-bit)
C (8-bit)
D (8-bit)
E (8-bit)
H (8-bit)
L (8-bit)
PC (16-bit)
SP (16-bit)
S | Z |  | A C |  | P |  | C Y
General Purpose Registers
Index Registers
Accumulator
Flag Register / Program Status Word (PSW)
S = Sign, Z = Zero, CY = Carry, AC = Auxiliary Carry, P = Parity,

## Slide 28: Addressing Modes
Microprocessor executes the instructions stored in memory (RAM).
It executes one instruction at a time.
Each of the instruction contains operations and operands.
Operation specifies the type of action to be performed.
  For example: ADD, SUB, MOV, INC, LOAD, STORE
Operands are the data on which the operation is to be performed.
MOV B, A ADD B
Here MOV is operation and (B & A) are operands.
Here ADD is operation and (B) is operand.

## Slide 29: Addressing Modes
Operand can be place either in one of the processor register or in
memory.
There are different ways to get the operands.
The way in which the operand is taken from register or memory is named as addressing mode.

## Slide 30: Addressing Modes
Immediate Addressing Mode
Register Addressing Mode
Register Indirect Addressing Mode
Direct Addressing Mode
Indirect Addressing Mode
Implied Addressing Mode
Relative Addressing Mode
Indexed Addressing Mode
Base Register Addressing Mode
Autoincrement or Autodecrement Addressing Mode

## Slide 31: 1. Immediate Addressing Mode
The operand is specified with in the instruction.
Operand itself is provided in the instruction rather than its address.
Move Immediate
MVI A , 15h A ← 15h
Here 15h is the immediate operand
Add Immediate
ADI 3Eh
A ← A + 3Eh
Here 3Eh is the immediate operand

## Slide 32: 2. Register Addressing Mode
The operand is specified with in one of the processor register.
Instruction specifies the register in which the operand is stored.
Move
C ← A Here A is the operand specified in register
MOV C , A
Add
Here B is the operand specified in register
ADD B
A ← A + B

## Slide 33: 3. Register Indirect Addressing Mode
The instruction specifies the register in which the memory address of operand is placed.
It do not specify the operand itself but its location with in the memory where operand is placed.
Move
A ← [[H][L]]
MOV A , M
It moves the data from memory location specified by HL register pair to A.

## Slide 34: 3. Register Indirect Addressing Mode
2807 | 
2806 | 
2805 | A9
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
H | 28
L | 05
2807 | 
2806 | 
2805 | A9
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
A | A9
MOV A , M A ← [[H][L]]
It moves the data from memory location specified by HL register pair to A.
Before After
A
H | 28
L | 05
A ← [2805]
A ← A9

## Slide 35: 4. Direct Addressing Mode
The instruction specifies the direct address of the operand.
The memory address is specified where the actual operand is.
Load Accumulator
LDA 2805h A ← [2805]
It loads the data from memory location 2805 to A.
Store Accumulator
STA 2803h [2803] ← A
It stores the data from A to memory location 2803.

## Slide 36: 4. Direct Addressing Mode
LDA 2805h A ← [2805]
It loads the data from memory location 2805 to A.
Before After
2807 | 
2806 | 
2805 | 5C
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
A
2807 | 
2806 | 
2805 | 5C
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
A | 5C
A ← [2805]
A ← 5C

## Slide 37: 4. Direct Addressing Mode
STA 2803h [2803] ← A
It stores the data from A to memory location 2803.
Before After
2807
2806
2805
2804
2803
2802
2801
2800
A | 9B
2807 | 
2806 | 
2805 | 
2804 | 
2803 | 9B
2802 | 
2801 | 
2800 | 
A | 9B
[2803] ← A
[2803] ← 9B

## Slide 38: 5. Indirect Addressing Mode
The instruction specifies the indirect address where the effective address of the operand is placed.
The memory address is specified where the actual address of operand is placed.
Move
MOV A, 2802h A ← [[2802]]
It moves the data from memory location specified by the location 2802 to A.

## Slide 39: 5. Indirect Addressing Mode
MOV A, 2802h A ← [[2802]]
It moves the data from memory location specified by the location 2802 to A.
Before After
2807 | 
2806 | FF
2805 | 
2804 | 
2803 | 06
2802 | 28
2801 | 
2800 | 
A
2807 | 
2806 | FF
2805 | 
2804 | 
2803 | 06
2802 | 28
2801 | 
2800 | 
A | FF
A ← [[2802]]
A ← FF

## Slide 40: 6. Implied Addressing Mode
It is also called inherent addressing mode.
The operand is implied by the instruction.
The operand is hidden/fixed inside the instruction.
Complement Accumulator CMA
(Here accumulator A is implied by the instruction)
Complement Carry Flag CMC
(Here Flags register is implied by the instruction)
Set Carry Flag STC
(Here Flags register is implied by the instruction)

## Slide 41: 7. Relative Addressing Mode
In relative addressing mode, contents of Program Counter PC is added to address part of instruction to obtain effective address.
The address part of the instruction is called as offset and it can +ve or –ve.
When the offset is added to the PC the resultant number is the memory location where the operand will be placed.

## Slide 42: 7. Relative Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
PC | 2801
Offset = 04h
Effective address of operand = PC + 01 + offset
Effective address of operand = 2801 + 01 + 04
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Actual Operand

## Slide 43: 7. Relative Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
PC | 2803
Offset = 03h
Effective address of operand = PC + 01 + offset
Effective address of operand = 2803 + 01 + 03
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Actual Operand

## Slide 44: 8. Indexed Addressing Mode
In index addressing mode, contents of Index register is added to address part of instruction to obtain effective address.
The address part of instruction holds the beginning/base address and is called as base.
The index register hold the index value, which is +ve.
Base remains same, the index changes.
When the base is added to the index register the resultant number is the memory location where the operand will be placed.

## Slide 45: 8. Indexed Addressing Mode
2800h + 0001h = 2801h
2800h + 0002h = 2802h
2800h + 0000h = 2800h
2800h + 0003h = 2803h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0000
Base = 2800h
Effective address of operand = Base + IX
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0001
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0002
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0003

## Slide 46: 8. Indexed Addressing Mode
2802h + 0001h = 2803h
2802h + 0002h = 2804h
2802h + 0000h = 2802h
2802h + 0003h = 2805h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0000
Base = 2802h
Effective address of operand = Base + IX
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0001
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0002
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0003

## Slide 47: 9. Base Register Addressing Mode
In base register addressing mode, contents of base register is added to address part of instruction to obtain effective address.
It is similar to the indexed addressing mode except the register now is called as base instead of index.
The base register hold the beginning/base address.
The address part of instruction holds the offset.
Offset remains same, the base changes.
When the offset is added to the base register the resultant number is the memory location where the operand will be placed.

## Slide 48: 9. Base Register Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Base | 2800
Offset= 0001h
Effective address of operand = Base Register + offset
2800h + 0001h = 2801h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2801h + 0001h = 2802h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2802h + 0001h = 2803h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2803h + 0001h = 2804h
Base | 2801
Base | 2802
Base | 2803

## Slide 49: 9. Base Register Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Base | 2800
Offset= 0003h
Effective address of operand = Base Register + offset
2800h + 0003h = 2803h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2801h + 0003h = 2804h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2802h + 0003h = 2805h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2803h + 0003h = 2806h
Base | 2801
Base | 2802
Base | 2803

## Slide 50: 10. Autoincrement or Autodecrement Addressing Mode
It is similar to register indirect addressing mode.
Here the register is incremented or decremented before or after its value is used.

## Slide 51: 10. Autoincrement or Autodecrement Addressing Mode
1st Time
2nd Time
3rd Time
4th Time
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2802
At start:
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2803
HL | 2804
HL | 2805
HL pair incremented after its value is used
HL | 2802

## Slide 52: 10. Autoincrement or Autodecrement Addressing Mode
1st Time
2nd Time
3rd Time
4th Time
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2803
At start:
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2805
HL | 2806
HL | 2807
HL pair incremented before its value is used
HL | 2804

## Slide 53: Discussion problem
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
Address
200
201
202
Memory
399
400
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
PC = Program Counter R1 = Register
XR = Index Register AC = Accumulator
Memory is having first instruction to load AC
Mode will specify the addressing mode to get operand.
Address field of instruction is 500.
Find out the effective address of operand and operand value by considering different addressing modes.

## Slide 54: Example problem
Address Memory
200
201
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
202
399
400
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
1. Immediate Addressing Mode
As instruction contains immediate number 500.
It is stored as address 201.
Effective Address = 201
Operand = 500
AC | 500

## Slide 55: Example problem
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
Address
200
201
202
Memory
399
400
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
2. Register Addressing Mode
Register R1 contains 400.
As operand is in register so no any memory location.
Effective Address = Nil
Operand = 400
AC | 400

## Slide 56: Example problem
Address
200
201
202
Memory
399
400
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
3. Register Indirect Addressing Mode
Register R1 contains 400.
So effective address of operand is 400.
The data stored at 400 is 700.
Effective Address = 400
Operand = 700
AC | 700

## Slide 57: Example problem
Address
200
201
202
Memory
399
400
500
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
600
702
PC | 200
R1 | 400
XR | 100
AC
800
4. Direct Addressing Mode
Instruction contains the address 500.
So effective address of operand is 500.
The data stored at 500 is 800.
Effective Address = 500
Operand = 800
AC | 800

## Slide 58: Example problem
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
Address
200
201
202
Memory
399
400
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
5. Indirect Addressing Mode
Instruction contains the address 500.
Address at 500 is 800.
So effective address of operand is 800.
The data stored at 800 is 300.
Effective Address = 800 Operand = 300
AC | 300

## Slide 59: Example problem
Address
200
201
202
Memory
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
6. Relative Addressing Mode
PC = 200.
Offset = 500.
Instruction is of 2 bytes.
So effective address = PC + 2 + offset = 200 + 500 +2 = 702 .
The data stored at 702 is 325.
Effective Address = 702 Operand = 325
AC | 325

## Slide 60: Example problem
Address
200
201
202
Memory
399
400
500
600
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
702
PC | 200
R1 | 400
XR | 100
AC
800
7. Index Addressing Mode
XR = 100.
Base = 500.
So effective address = Base + XR = 500 + 100 = 600 .
The data stored at 600 is 900.
Effective Address = 600 Operand = 900
AC | 900

## Slide 61: Example problem
Address
200
201
202
Memory
399
400
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
8. Autoincrement Addressing Mode
It is same as register indirect addressing mode except the contents of R1 are incremented after the execution.
R1 contains 400.
So effective address of operand is 400.
The data stored at 400 is 700.
Effective Address = 400 Operand = 700
AC | 700
R1 | 401

## Slide 62: Example problem
Address
200
201
202
Memory
399
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
400
500
600
702
PC | 200
R1 | 400
XR | 100
AC
800
9. Autodecrement Addressing Mode
It is same as register indirect addressing mode except the contents of R1 are decremented before the execution.
R1 contains 400.
R1 is first decremented to 399.
So effective address of operand is 399.
The data stored at 399 is 450.
Effective Address = 399 Operand = 450
AC | 450
R1 | 399

## Slide 63: Solution for problem
Ali Asghar Manjotho, Lecturer CSE-MUET
Addressing Mode | Effective Address | Operand
Immediate Addressing Mode | 201 | 500
Register Addressing Mode | Nil | 400
Register Indirect Addressing Mode | 400 | 700
Direct Addressing Mode | 500 | 800
Indirect Addressing Mode | 800 | 300
Relative Addressing Mode | 702 | 325
Indexed Addressing Mode | 600 | 900
Autoincrement Addressing Mode | 400 | 700
Autodecrement Addressing Mode | 399 | 450

## Slide 64: INSTRUCTION TYPES

## Slide 65: Instruction Types

## Slide 66: Instruction Types…

## Slide 67: Instruction Types…

## Slide 68: Instruction Types…