## Slide 1: Module 3 Part B
Single Cycle Data Path - Multi Cycle Data Path
Dr. Abdul Quadir Md, SCOPE
VIT Chennai

## Slide 2: Data Path Architecture Introduction

## Slide 3: Data Path Architecture
Highest Level : Program
.
.
.
Lowest Level : State
At each state small activity happens
(RTL Activities)
(Register Transfer Level Activities)
RTL: The Sequence in which the register transfer actions should take place will be decided by the controller

## Slide 4: Data Path Architecture
Activity consist of
i) Data Path : How a data travels inside the processor from one component to a another component
ii) Control (Controlling the Data Path): Who is controlling the data and who decides which path it has to take

## Slide 5: Data Path Typical Architecture
2. Controller will issue appropriate signals
1. Architecture means : How you can put the various components together so that whenever the processor needs
3. Physical connections will be enabled
4. That data will move around

## Slide 6: Components of Data Path Architecture
Multiplexer
ALU
Registers

## Slide 7: Multiplexer
Multiple inputs
One output
Which one output from many inputs will be selected, will be decided by the select line (otherwise called as controller).

## Slide 8: ALU (Arithmetic and Logic Unit)
For example, a 32 ALU can perform:
16 Arithmetic Operations
16 Logical Operations
5 bit control lines to select any one of the ALU operations
ALU performs the role of both Mux and ALU

## Slide 9: Registers
General Purpose Registers (GPR) are the ones which stores the data on the processors side
Example, R0, R1, R2… Rn

## Slide 10: Single Cycle Data Path Architecture

## Slide 11: Execution of Complete Instruction Using Single Cycle Data Path
The whole control sequence for the instruction( ins) execution Add R1 , (R2) for the single cycle data path is explained
The instruction value of the register (reg) R1 and the value of the memory place indicated by the reg R2 is added
The result is stored in the register R1

## Slide 12: Execution of Single Cycle Data Path(Conti..)
To execute the Add R1 , (R2) instruction the following actions are necessary
Obtain the instruction from the memory location
Obtain the operand from the memory location directed by R2
Carry out the ALU operation indicated by the instruction (i.e add in this example)
Store the end result in R1

## Slide 13: Figure 1. Single Cycle Data Path Architecture
Reference: Hamacher, C., Vranesic, Z., & Zaky, S. (2002). Computer organization. McGraw-Hill.

## Slide 14: Control steps - Add R1 , (R2) - Explanation
Step1: The inst fetch step is performed by placing the value of the PC in MAR and Read signal is activated PC  MAR
At the same instance, PC value are also placed in Y reg and added with const integer by triggering the select C i/p of mux and add i/p of the ALU PCPC+1
When Zin signal is activated the output is put in Z reg CONSTANT  Z

## Slide 15: Control steps - Add R1 , (R2) - Explanation
Step2: The Z reg value are moved to PC reg by actuating Zout and PC in
signal Z  PC
By doing this, PC increment process is completed and PC will indicate to next inst
WMFC: Wait Till Memory Function Complete, will wait till memory replies the request of fetch instruction to the processor. WMFC
Once WMFC signal is received from the memory , the contents of the specified location are available in MDR register inside the processor

## Slide 16: Control steps - Add R1 , (R2) - Explanation
Step3: The contents of register MDR are moved to reg IR of the CPU MDR  IR
Step 1, 2 and 3 forms the inst fetch stage
In Step 4, inst decoder decodes the IR contents
Step 4, 5, 6, and 7 forms the instruction execution phase

## Slide 17: Control steps - Add R1 , (R2) - Explanation
Step4: The value of reg R2 are moved to MAR , by actuating R2, out & MARin signal R2 MAR
Read signal is activated

## Slide 18: Control steps - Add R1 , (R2) - Explanation
Step5: Reg R1 value are moved to Y reg by actuating R1, out and Yin signal R1 Y
After WMFC signal is received , the contents of the specified location are available in MDR

## Slide 19: Control steps - Add R1 , (R2) - Explanation
Step6: MDR out, select Y, Add and Zin signals are actuated to perform by adding of values of reg Y and MDR. MDR,Y Z in
Step7: The contents of register Z are moved to R1 ZR1
End function triggers a new inst to take the new instruction fetch cycle to begin

## Slide 20: Sequence of control steps using single cycle for Add R1 , (R2)
Reference: Hamacher, C., Vranesic, Z., & Zaky, S. (2002). Computer organization. McGraw-Hill.

## Slide 21: Multi Cycle Data Path Architecture

## Slide 22: Why Multi Cycle Data Path ?
In a single cycle data path architecture , exclusively single data word could be moved through the bus in a given clock cycle
Because of this no of steps needed to execute the inst increases
To decrease the no of steps needed to execute the inst and to transfer more than one word in a clock cycle we go for multicycle

## Slide 23: How Multi Cycle Data Path Works
Three buses are used to link reg and ALU of the CPU
All GPR ,
R1, R2…Rn are presented in one block known as reg files
Figure 2. shows the register files has three ports

## Slide 24: Figure 2. Multi Cycle Data Path Architecture
Reference: Hamacher, C., Vranesic, Z., & Zaky, S. (2002). Computer organization. McGraw-Hill.

## Slide 25: How Multi Cycle Data Path Works
One input and two output ports
Therefore data of three registers are possible to access in single clk cycle
Through Bus C, the value could be put in one reg
Data from two regs is available through Bus A and Bus B

## Slide 26: How Multi Cycle Data Path Works
Bus A and B are used to move the source operands to i/ps of the ALU A and B
After ALU process is executed the resultant is moved to destination operand through the bus C
Separate incremental unit is provided to increment the value of PC after every instruction is executed

## Slide 27: Execution of Instruction using Multi Cycle Data Path Add R1, R2, R3 Control Sequence
The inst adds the values of register R2 & R3 and stores the resultant in R1

## Slide 28: Multi Cycle Data Path Add R1, R2, R3 Control Sequence Explanation
Step 1: The value of the PC are moved to MAR by means of Bus B to begin Read operation. PCMAR
Parallelly PC is incremented point towards the next instruction PCPC+1

## Slide 29: Multi Cycle Data Path Add R1, R2, R3 Control Sequence Explanation
Step 2: The processor waits for WMFC signal from the memory
Step 3: The inst code is moved from MDR to IR MDR IR
Step 4: The inst decoder decodes the IR contents

## Slide 30: Multi Cycle Data Path Add R1, R2, R3 Control Sequence Explanation
Step 4: Two values from reg R2 & R3 are made accessible at inputs A and B of ALU by means of Bus A & B
By activating the Add signal two inputs are added
Through Bus C the resultant is stored in R1

## Slide 31: Multi Cycle Data Path Add R1, R2, R3 Control Sequence Explanation
By providing more data paths it is possible to reduce number of clock cycles needed to execute an instruction

## Slide 32
Any Questions ?

## Slide 33: References
Hamacher, C., Vranesic, Z., & Zaky, S. (2002). Computer organization. McGraw-Hill.

## Slide 34
Thank You!